## Slide 1: Automatic DCS for the best quality
Excellent firmness, long shelf live,
Protection against scald, pit rot, skin spot,
Alternative for smartfresh,
Natural ripening, excellent taste.

## Slide 2: The advantages of DCS
Maximum reduction of scald, skin spots and pit rot
Better firmness, better shelf life
Non chemical treatment
Natural ripening after storage, better taste
Better appearance of the product
DCSTM represents a quality label
DCS can be used as an alternative for smartfresh / or be used in combination with smartfresh.
Guarantees on freshness and quality can be realized on a better way.

## Slide 3: What is Automatic DCS?
It provides an automatic system for daily accurate measuring of the ethanol production on a ppb level of a sample of fruit.
The fruit can be stored at the lowest O2 level where fermentation will not start.
Storing fruit at the lowest O2 level will provide the best fruit quality;
Measuring fluorescence, respiration or other indirect factors provide indirect, less accurate information

## Slide 4: Why automatic DCS?
Ethanol is the
only direct
marker for DCS/ DCA storage
(other markers are working indirect for indicating fermentation.)

## Slide 5: 2 pc. Measuring boxes with gasanalyser connected on 2 rooms

## Slide 6
Installation of measuring boxes

## Slide 7: Installation of measuring boxes

## Slide 8: Ventilation opening

## Slide 9
5. The graph shows a clear picture of the trend of the ethanol production of the sample per day. The daily reports gives the operator essential information for safe and reliable storing fruit at the lowest O2 levels.
How does it work

## Slide 10
5. The operator will maintain, reduce or increase the O2 level in this CA store depending on the strategy and the measurement results.
6. Relevant information of the fruit stored in the DCS room is stored in a web based portal and is easy accessible for the operator and his staff, the consultant and the supplier. Relevant information can be added to this database and consulted by this persons.
How does it work

## Slide 11: The system sends each day an email with the measured ethanol and O2 values

## Slide 12: How the day starts with DCS

## Slide 13: Example ethanol production
The O2 level is ca. 0,2%. The Ethanol production rises to 0,6 ppb, which is still rather low.

## Slide 14: Example ethanol production
A further increase to 1,4ppb.

## Slide 15: Example ethanol production
We did 3x an fruit flesh analyze. At 2-3 ppb ethanol there was no ethanol present. At 8 ppb there was 8 mg Ethanol/100 gr. fruit flesh, at 20 ppb we measured ca. 17 mg ethanol / 100 gr. fruit flesh.

## Slide 16
The lowest O2% will vary;
  per origin / variety
  Per season
The lowest O2% can change during the storage season. (dynamic)
Characteristics

## Slide 17
A daily and reliable report about the ethanol production of your fruit.
Daily protection/security for the storage of your fruit on the lowest oxygen levels.
Automatic DCS can be used as:
  A watchdog system
  A dynamic system for storage at the lowest oxygen levels
Characteristics

## Slide 18
Measuring ethanol provides the only direct measured value for indicating the lowest O2% where at fermentation starts.
Ethanol is the best marker for fermentation.
Characteristics

## Slide 19: Extra advantages of Automatic DCS
Faster to the lowest oxygen levels
In comparison with all others systems: a daily control on ethanol production of the fruit at de lowest oxygen levels.

## Slide 20: Extra advantages of Automatic DCS
The best fruit quality after storage is archieved by storage at the lowest oxygen levels (source: FBR Wageningen)

## Slide 21: Facts about DCS
DCS and Automatic DCS are researched for years and has proved themselves
After the introduction of DCS in 1997, alternative systems are introduced below the name of DCA (Dynamic Controlled Atmosphere)
DCS gives in comparison with the normal ULO storage systems better results.
DCS can be used as a alternative of Smartfresh, or in combination with Smartfresh

## Slide 22: History of DCSTM
DCS is developed and introduced by Wageningen UR, Food & Biobased Research, Netherlands since 1997.
Since 1997 more than 15 years of research
DCS is applied in ca. 200 cells.
DCS is applied in ca. 200 cellen. Checking the apples on the presence of ethanol is carried out manually by a pulp analysis
When there is no ethanol measured, the oxygen level can be decreased. When ethanol is measured the oxygen level has to increase. Dynamic storage.

## Slide 23: History of DCSTM
A number of attempts to automate the DCS system has failed
Due to the labour-intensive method, the semi automatic DCS application is used very limited. This despite the enormous advantages
Due to the labour-intensive DCS storage, most oxygen values aren’t reached as soon as possible
Automic DCS makes it possible to control and reach the oxygen levels quickly
DCS improves the quality of the fruit by long term storage.

## Slide 24: DCS - History
Before automatic DCS, there was no reliable measurement for ethanol in a cold store. Why?
Ethanol has to be measured on ppb scale
Measuring ethanol is difficult, because of the presence of, for example ethylene and other gasses.
Ethanol dissolves easily in water
Also rotting fruit produces ethanol
Because of the developed procedure with the measuring box this problems haven been solved.

## Slide 25: History of the DCS Automatic
  Since 2009 there is a cooperation between:
  Wageningen UR, Food & Biobased Research, Nederland
  Storex B.V.
  EMS B.V. ( Manufacturer of analytic sensor technics)
  Since 2009 we have devolped the Automatic DCS system, based on new developed sensor technics
  Since 2013 the system is ready to be used

## Slide 26: Research results
Remarkable results of research in Canada 2013/2014 with McIntosch
After 7 days on room temperature, apples stored with DCS maintain the same firmness as apples stored with ULO and Smartfresh.

## Slide 27
Elstar
Firmness ULO versus DCSTM

## Slide 28
Distribution of firmness ULO versus DCSTM

## Slide 29
DCSTM versus SmartFresh
Firmness distribution after 7,5 months storage and 7 days shelf
ULO and DCS storage with and without SmartFresh – Elstar Q2 H2
Firmnessgrade (per 0,5) kg))
Fruit fraction %

## Slide 30
Scald control

## Slide 31
Reduction of schil spots

## Slide 32
Configuration
O2 / CO2 CONTROL
O2 / CO2 SENSORS
ETHANOL
DCS Sample box
DATA-LOGGING
OPTIMAL O2
DCS ANALYZER

## Slide 33
DCSTM components
The sample boxes
  Two pieces of solid sample boxes
  Transparant perspex lid for visual inspection and accessibility
  Sample boxes can be built into the ceiling and side wall of the cold store
  Equipped with a ventilation opening which can be closed with a membrane

## Slide 34: Automatic DCS is now available
Automatic DCS is now available to use.
The offer in 2014 consists for each system:
  2 pc. of sample boxes
  The DCS ethanol measuring system
  A license-free use of the system
  When you are interested, we would be happy to plan a meeting with you. During this meeting we will make the DCS system available for your company. So you can benefit of the advantages of the DCS system.